## Slide 1: NUMBER SYSTEM Lesson 1
By Prasad Weerathunga

## Slide 2: INTRODUCTION TO NUMBERING SYSTEMS
We are all familiar with the decimal number system (Base 10). Some other number systems that we will work with are:
  Binary  Base 2
  Octal  Base 8
  Hexadecimal  Base 16

## Slide 3: Characteristics of Numbering Systems
The digits are consecutive.
The number of digits is equal to the size of the base.
Zero is always the first digit.
The base number is never a digit.
When 1 is added to the largest digit, a sum of zero and a carry of one results.
Numeric values are determined by the implicit positional values of the digits.

## Slide 4: The Decimal Number System
Name
“decem” (Latin) => ten
Characteristics
Ten symbols
  0 1 2 3 4 5 6 7 8 9
Positional
  2945 ≠ 2495
  2945 = (2*103) + (9*102) + (4*101) + (5*100)
(Most) people use the decimal number system
Why?

## Slide 5: The Binary Number System
Name
“binarius” (Latin) => two
Characteristics
Two symbols
  0 1
Positional
  1010B ≠ 1100B
Most (digital) computers use the binary number system
Why?
Terminology
Bit: a binary digit
Byte: (typically) 8 bits

## Slide 6: Memory cell used by a computer
One switch can be in one of 2 states
A row of n switches:
can be in one of 2n states !
A row of 3 switches can be in one of 23 = 8 states.
The 8 possible states are given in the figure above.

## Slide 7: Memory cell used by a computer
We saw how information can be represented by number by using a code (agreement)
Recall: we can use numbers to represent marital status information:
0 = single
1 = married
2 = divorced
3 = widowed

## Slide 8: BINARY NUMBER SYSTEM
Also called the “Base 2 system”
The binary number system is used to model the series of electrical signals computers use to represent information
0 represents the no voltage or an off state
1 represents the presence of voltage or an
on state

## Slide 9: Binary Numbering Scale
Base 2 Number | Base 10 Equivalent | Power | Positional Value
000 | 0 | 20 | 1
001 | 1 | 21 | 2
010 | 2 | 22 | 4
011 | 3 | 23 | 8
100 | 4 | 24 | 16
101 | 5 | 25 | 32
110 | 6 | 26 | 64
111 | 7 | 27 | 128

## Slide 10: Decimal to Binary Conversion
The easiest way to convert a decimal number to its binary equivalent is to use the Division Algorithm
This method repeatedly divides a decimal number by 2 and records the quotient and remainder
  The remainder digits (a sequence of zeros and ones) form the binary equivalent in least significant to most significant digit sequence

## Slide 11: Decimal to Binary Conversion
Convert 67 to its binary equivalent:
6710 = x2
Step 1: 67 / 2 = 33 R 1 Divide 67 by 2. Record quotient in next row
Step 2: 33 / 2 = 16 R 1 Again divide by 2; record quotient in next row
Step 3: 16 / 2 = 8 R 0 Repeat again
Step 4: 8 / 2 = 4 R 0 Repeat again
Step 5: 4 / 2 = 2 R 0 Repeat again
Step 6: 2 / 2 = 1 R 0 Repeat again
Step 7: 1 / 2 = 0 R 1 STOP when quotient equals 0
1 0 0 0 0 1 12

## Slide 12: Decimal to Binary Conversion
Example
Find what is binary value of following decimals?
75
133
1573

## Slide 13: Binary Number Addition
Addition
Results are mod 24
7
+ 10
--
1
11
0111B
+ 1010B
---- 10001B
1 3 0011B |  |  | 
+ | 10 -- | + | 1010B ----
 | 13 |  | 1101B
Start at right column Proceed leftward
Carry 1 when necessary

## Slide 14: Binary Number Subtraction
Subtraction
Results are mod 24
3
- 10
--
9
2
0011B
- 1010B
---- 1001B
10
- 7
--
3
12
0202
1010B
- 0111B
----
0011B
Start at right column Proceed leftward
Borrow 2 when necessary

## Slide 15
Example
Find addition of following binary numbers?
1012 + 1102
101012 + 111002
1110112 + 1101102
Find substraction of following binary numbers?
111112 - 100112 =1100
1011002 - 1001102 = 110
1111112 - 1001112 =11000

## Slide 16: Binary to Decimal Conversion
The easiest method for converting a binary number to its decimal equivalent is to use the Multiplication Algorithm
Multiply the binary digits by increasing powers of two, starting from the right
Then, to find the decimal number equivalent, sum those products

## Slide 17
Convert (10101101)2 to its decimal equivalent:
Binary 1 0 1 0 1 1 0 1
Positional Values
x
x
x
x
x
x
x
x
20
21
22
23
24
25
26
27
128 + 32 + 8 + 4 + 1
Products
17310
Binary to Decimal Conversion

## Slide 18
Binary to Decimal Conversion
Example
Find what is Decimal value of following binary numbers?
10110 =22
100101 =37
110101 =53
11001102 = 1×26 + 1×25 + 0×24 + 0*23 + 1*22 + 1×21 + 0*20 = 64 + 32 + 4 + 2 = 102.

## Slide 19: (10110)₂ = (1 × 2⁴) + (0 × 2³) + (1 × 2²) + (1 × 2¹) + (0 × 2⁰) = 22₁₀
(100101)₂ = (1 × 2⁵) + (0 × 2⁴) + (0 × 2³) + (1 × 2²) + (0 × 2¹) + (1 × 2⁰) = 37₁₀
(110101)₂ = (1 × 2⁵) + (1 × 2⁴) + (0 × 2³) + (1 × 2²) + (0 × 2¹) + (1 × 2⁰) = 53₁₀

## Slide 20: OCTAL NUMBER SYSTEM
Also known as the Base 8 System
Uses digits 0 - 7
Readily converts to binary
Groups of three (binary) digits can be used to represent each octal digit
Also uses multiplication and division algorithms for conversion to and from base 10

## Slide 21: Decimal-Octal Equivalence
Decimal | Octal |  | Decimal Octal |  | Decimal | Octal
0 | 0 |  | 16 20 |  | 32 | 40
1 | 1 |  | 17 21 |  | 33 | 41
2 | 2 |  | 18 22 |  | 34 | 42
3 | 3 |  | 19 23 |  | 35 | 43
4 | 4 |  | 20 24 |  | 36 | 44
5 | 5 |  | 21 25 |  | 37 | 45
6 | 6 |  | 22 26 |  | 38 | 46
7 | 7 |  | 23 27 |  | 39 | 47
8 | 10 |  | 24 30 |  | 40 | 50
9 | 11 |  | 25 31 |  | 41 | 51
10 | 12 |  | 26 32 |  | 42 | 52
11 | 13 |  | 27 33 |  | 43 | 53
12 | 14 |  | 28 34 |  | 44 | 54
13 | 15 |  | 29 35 |  | 45 | 55
14 | 16 |  | 30 36 |  | 46 | 56
15 | 17 |  | 31 37 |  | 47 | 57
 |  |  |  |  | ... | ...

## Slide 22: Decimal-Octal Conversion
Octal to decimal: expand using positional notation
Decimal to octal: use the shortcut
37O = (3*81) + (7*80) = 24 + 7 |  |  | 
= | 31 |  | 
31 / 8 = 3 R 7
3 / 8 = 0 R 3

## Slide 23
Example
Find what is Octal value of following decimals?
75610
135110
35210
Find what is decimal value of following Octals?
3518
21368
1578

## Slide 24
Division by 8 | Quotient | Remainder (Digit)
(756)/8 | 94 | 4
(94)/8 | 11 | 6
(11)/8 | 1 | 3
(1)/8 | 0 | 1
Division by 8 | Quotient | Remainder (Digit)
(1351)/8 | 168 | 7
(168)/8 | 21 | 0
(21)/8 | 2 | 5
(2)/8 | 0 | 2
Division by 8 | Quotient | Remainder (Digit)
(352)/8 | 44 | 0
(44)/8 | 5 | 4
(5)/8 | 0 | 5

## Slide 25: 351 = (3 × 8²) + (5 × 8¹) + (1 × 8⁰) = 233
2136 = (2 × 8³) + (1 × 8²) + (3 × 8¹) + (6 × 8⁰) = 1118
157 = (1 × 8²) + (5 × 8¹) + (7 × 8⁰) = 111

## Slide 26: Octal Number Addition
Addition
20368
+ 57628
---- 100208
42108
+ 26718
---- 71018
Example
Find addition of following Octal numbers?
53768 + 36578 = 112558
4358 + 3428 = 7778
4718 + 2428 = 7338

## Slide 27: Octal Number Subtraction
Subtraction
3758
- 1268
----
6528
4718
- 5368
----
2428
Example
Find addition of following Octal numbers?
14638 - 11028 =361
256168 - 175208 =6076
156778 - 72608 =6417

## Slide 28: HEXADECIMAL NUMBER SYSTEM
Base 16 system
Uses digits 0-9 &
letters A,B,C,D,E,F
Groups of four bits represent each base 16 digit

## Slide 29: Decimal to Hexadecimal Conversion
Convert 83010 to its hexadecimal equivalent:
830 / 16 = 51 R14
51 / 16 = 3 R3
3 / 16 = 0 R3
33E16
= E in Hex

## Slide 30: Hexadecimal to Decimal Conversion
Convert 3B4F16 to its decimal equivalent:
Hex Digits
3 B 4 F
x
x
x
163 162 161 160
12288 +2816 + 64 +15
15,18310
Positional Values
Products
x

## Slide 31
Example
Find what is Hexadecimal value of following decimals?
75110
506710
93610
Find what is decimal value of following Hexadecimals?
A3F16
29FC16
8C616

## Slide 32
Division by 16 | Quotient | Remainder (Digit)
(751)/16 | 46 | 15
(46)/16 | 2 | 14
(2)/16 | 0 | 2
Division by 16 | Quotient | Remainder (Digit)
(5067)/16 | 316 | 11
(316)/16 | 19 | 12
(19)/16 | 1 | 3
(1)/16 | 0 | 1
= (13CB)16
= (2EF)16
Division by 16 | Quotient | Remainder (Digit)
(936)/16 | 58 | 8
(58)/16 | 3 | 10
(3)/16 | 0 | 3
= (3A8)16

## Slide 33: (A3F)₁₆ = (10 × 16²) + (3 × 16¹) + (15 × 16⁰) = (2623)₁₀
(29FC)₁₆ = (2 × 16³) + (9 × 16²) + (15 × 16¹) + (12 × 16⁰) = (10748)₁₀
(8C6)₁₆ = (8 × 16²) + (12 × 16¹) + (6 × 16⁰) = (2246)₁₀

## Slide 34: Hexadecimal Number Addition
Addition
A3416
+ 8E916
----
131D16
25D316
+ C85F16
----
EE3216
Example
Find addition of following Octal numbers?
9D316 + 2EF16
A30116 + 48916
EAB5816 + B28716

## Slide 35: Hexadecimal Number Subtraction
Subtraction
B3CD16
+ 849A16
----
2F3316
85AD16
+ 5EOF16
----
279E16
Example
Find addition of following Octal numbers?
F2CD316 - 846C16
82416 - A3516
A2CD16 - 9BFC16

## Slide 36: Binary-Hexadecimal Conversion
Observation: 161 = 24
Every 1 hexadecimal digit corresponds to 4 binary digits
Binary to hexadecimal
1010000100111101B A 1 3 DH
Digit count in binary number not a multiple of 4 =>
pad with zeros on left
Hexadecimal to binary
A 1 3 DH 1010000100111101B
Discard leading zeros from binary number if appropriate

## Slide 37: Binary-Hexadecimal Conversion
The easiest method for converting binary to hexadecimal is to use a substitution code
Each hex number converts to 4 binary digits

## Slide 38: Binary-Octal Conversion
Observation: 81 = 23
Every 1 octal digit corresponds to 3 binary digits
Binary to octal
001010000100111101B
1 2 0 4 7 5O
Digit count in binary number not a multiple of 3 =>
pad with zeros on left
Discard leading zeros from binary number if appropriate
Octal to binary
1 2 0 4 7 5O
001010000100111101B

## Slide 39: THANK YOU